## Slide 1: TF map from scratch
Practice

## Slide 2: Task specification
Do not use external toolbox
In-built function in MATLAB signal processing toolbox is allowed
Borrow codes from signal analysis book is encouraged
Google solution NOT Baidu

## Slide 3: Task one
Plot the third channel
Zoom in and check the pulses

## Slide 5: Task two
Rereference the first 2 channels in a bipolar manner and plot the raw and rereferenced channel like below (2-5s segment)
Don’t forget the baseline normalization of the segment

## Slide 7: Task three
Filter the bipolar referenced signal to different frequency band and plot them with raw signal like below (2-5s segment)
Band:
Delta < 4Hz
Theta 4–7
Alpha 8–15
Beta 16–31
Gamma > 32
High Gamma 70-170

## Slide 9: Task four
Extract time stamps from DC channels and epoch bipolar channel
Plot all the epoched traces together [-600ms to 1600ms]

## Slide 12: Task five
Time frequency transform of the epoched data.
Short time Fourier or Gabor wavelet
Frequency range: 0:1:200Hz
Baseline: [-500:0]ms; Signal: [0:1500]ms
Plot any 6 trials time frequency map in separate figures.
Plot the averaged TF map in one figure

## Slide 15: Task six
Baseline normalization
Use Zscore normalization and percentage normalizaiton

## Slide 17: Task seven
Extract the power from 70 to 170Hz and plot the power traces